## Slide 1
Laser Beam Alarm Security System with Blynk Cloud Monitoring & Gmail Alerts
Udayasai Ramineni(11802872)
Ashfaaq Ahamed Kapatrala(11786442)

## Slide 2
Laser Beam Alarm
Security System
with Blynk Cloud Monitoring & Gmail Alerts
Milestone 1: System Design & Hardware Justification
Raspberry Pi Pico W
LDR Sensor
Laser Module
Blynk IoT Cloud
Gmail SMTP
MicroPython
Project Motivation
Physical security systems are critical for protecting doorways, gates, and restricted areas.
This project enhances a classic laser trip-wire alarm by adding IoT capabilities:
>> Real-time sensor monitoring via Blynk Cloud
>> Instant push notifications to owner's phone
>> Automated Gmail alerts on intrusion detection
The result is a smart, remotely monitored embedded security system.
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
1 / 7

## Slide 3
System Architecture Diagram
Block diagram showing inputs, processing, outputs and data flow
POWER SUPPLY (USB 5V)
|
[Raspberry Pi Pico W]
RP2040 + CYW43439 Wi-Fi
|
ADC26 <-- LDR Sensor
GPIO2 --> Laser Module
GPIO4 --> Blue LEDs
GPIO5 --> Red LEDs
GPIO6 --> Buzzer
|
Wi-Fi 2.4 GHz
|
[Internet / Cloud]
| |
[Blynk Cloud] [Gmail SMTP]
[Dashboard ] [Alert Email]
INPUTS
• LDR Sensor — ADC detects laser presence
• Laser Module — focused beam source
PROCESSING
• Pico W polls LDR every 100ms
• Threshold comparison in firmware
• Alarm logic + cloud triggers
LOCAL OUTPUTS
• Buzzer — 85dB audible alarm
• Red LEDs — flashing on intrusion
• Blue LEDs — standby indicator
CLOUD OUTPUTS
• Blynk: live LDR graph + alarm flag
• Blynk: push notification to phone
• Gmail: intrusion alert email (SSL)
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
2 / 7

## Slide 4
Hardware Component Selection
All components with specifications, justification, and vendor URLs
Raspberry Pi Pico W
• RP2040 dual-core ARM Cortex-M0+ @ 133MHz
• Wi-Fi 802.11 b/g/n via CYW43439 chip
• 3x 12-bit ADC | 26 GPIO | 3.3V I/O
• Chosen: onboard Wi-Fi for Blynk + Gmail
• adafruit.com/product/5526
KY-008 Laser Module
• 650nm red laser, <5mW (Class IIIA)
• 5V DC, ~30mA current draw
• Digital ON/OFF GPIO control
• Chosen: focused beam, easy alignment
• amazon.com/dp/B01MAWT5JX
LDR Sensor
• Resistance: 1kOhm (light) to 1MOhm (dark)
• 3.3V-5V compatible | ~20ms response
• Direct ADC readout — no extra IC needed
• Chosen: simple, reliable beam-break detect
• adafruit.com/product/161
5V Active Buzzer
• 85 dB audible alarm output
• 5V DC, ~35mA via D400 transistor
• Simple HIGH/LOW control — no PWM needed
• Chosen: instant alarm, minimal firmware
• amazon.com/dp/B0716GH3QD
LEDs + Transistors + Resistors
• 4x Red + 4x Blue 5mm LEDs (10-20mA each)
• D400 NPN transistors switch LED + buzzer
• 180Ohm LED | 1kOhm base | 10kOhm LDR divider
• Transistors protect Pico W 12mA GPIO limit
• amazon.com/dp/B01AUI4VQU
Custom PCB (JLCPCB)
• Gate-shaped custom PCB design
• Eliminates breadboard wiring errors
• Fixed mounting for laser + LDR alignment
• LDR on adjustable female header
• jlcpcb.com
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
3 / 7

## Slide 5
IoT Features: Blynk Cloud + Gmail Alerts
Real-time monitoring and automated email notification on intrusion
Blynk Cloud Dashboard
• Persistent TCP socket maintained at startup
• V0 Pin: LDR ADC value sent every 2s -> live graph
• V1 Pin: Alarm flag (0=normal, 1=intruder)
• Push notification sent instantly to owner's phone
• Blynk auto-logs readings with timestamps
Gmail SMTP Alert
• SSL connection to smtp.gmail.com port 465
• Google App Password (2FA) — secure credentials
• Email: timestamp + Intruder Detected + LDR value
• 30-second cooldown prevents email flooding
• Sent async — local buzzer/LED triggers first
Alarm Event Data Flow
BEAM BROKEN
LDR ADC > Threshold (3 reads / 300ms)
v
INSTANT
Buzzer ON + Red LEDs Flash (local)
v
BLYNK
V1=1 sent + Push Notification to phone
v
GMAIL
SMTP SSL: Intrusion Alert Email sent
v
COOLDOWN
30s timer -> alarm resets -> normal mode
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
4 / 7

## Slide 6
Power Consumption Analysis
Component power budget, source justification, and efficiency strategies
Component
Current
Power
Bar
Raspberry Pi Pico W (Wi-Fi on)
100 mA
330 mW
Laser Module
30 mA
150 mW
Buzzer (when active)
35 mA
175 mW
LEDs x4 (when on)
40 mA
80 mW
LDR + Resistor Divider
0.3 mA
1 mW
TOTAL (worst case)
~736 mW
Power Source: USB 5V 2A Wall Adapter
• Indoor fixed install — 24/7 uptime required
• Continuous Wi-Fi drains battery in hours
• 5V/2A = 10W available — 13x headroom
Power Efficiency Strategies
• Blynk updates every 2s (not every 100ms poll)
• Wi-Fi radio in low-power listen mode between updates
• Blue LEDs at 30% PWM duty cycle in standby
• Buzzer energized only during active alarm events
• 10kOhm LDR pull-down limits quiescent current
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
5 / 7

## Slide 7
Integration Challenges & Solutions
Identified risks and concrete mitigation strategies
Wi-Fi Latency on Alarm
Problem: Wi-Fi connection at alarm time causes 2-5s notification delay.
Solution: Persistent Wi-Fi + Blynk TCP socket at startup. Local alarm triggers instantly.
LDR False Alarms
Problem: Ambient light changes cross the ADC threshold incorrectly.
Solution: Dynamic threshold at boot. Requires 3 consecutive crossings (300ms) before alarm.
Gmail SMTP Security
Problem: Google blocks SMTP with regular passwords; credentials in firmware are a risk.
Solution: Google App Password + SSL port 465. No plain-text credentials transmitted.
GPIO Current Limits
Problem: Pico W GPIO pins limited to 12mA - insufficient for buzzer and LED arrays.
Solution: D400 NPN transistors switch loads. GPIO drives only transistor base via 1kOhm.
Laser / LDR Alignment
Problem: Precise alignment across PCB gate required for reliable detection.
Solution: Custom gate PCB fixes mounting positions. LDR on adjustable header.
Email Flooding
Problem: Sustained beam interruption triggers continuous SMTP connections.
Solution: 30-second cooldown timer. One email per event; suppressed until beam restored.
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
6 / 7

## Slide 8
Summary & Next Steps
Milestone 1 deliverables complete — Milestone 2 hardware testing begins
Milestone 1 Goals Achieved
• System architecture fully defined with block diagram
• All hardware selected & justified with specs and URLs
• IoT extensions (Blynk + Gmail) designed & integrated
• Power budget calculated — USB 5V solution justified
• 6 integration challenges identified with concrete solutions
Milestone 2 Plan
• Order PCBs from JLCPCB and assemble all components
• Flash MicroPython firmware on Raspberry Pi Pico W
• Calibrate LDR threshold and verify laser alignment
• Integrate Blynk library — verify live dashboard
• Test Gmail SMTP alert with real intrusion events
Component Summary
Component
Vendor
~Cost
Raspberry Pi Pico W
Adafruit
$6
KY-008 Laser Module
Amazon
$5
LDR Sensor
Adafruit
$2
5V Active Buzzer
Amazon
$3
5mm LEDs (Red+Blue)
Amazon
$4
D400 Transistors
Amazon
$3
Resistor Kit
Amazon
$5
Custom PCB (x5)
JLCPCB
$8
Estimated Total Cost
~$36
CSCE 5612 | Embedded Hardware/Software Design | Spring 2026
7 / 7